## Slide 1: DOT ERG isolation and downwind distances and other models Tucson, AZ Disaster Response Scenario
John S. Morawetz
International Chemical Workers Union Council
Center for Worker Health & Safety Education
Cincinnati, Ohio
https://hsed.icwuc.org/
HMIT grant with UAW, AFSCME, AFGE and UFCW

## Slide 2
ERG: Background on Table 1
Initial Isolation and Protective Action Distances
p. 293: “determine the downward distance to which persons may become incapacitated and unable to take protective action or may incur serious health effects”

## Slide 3: DOT ERG Initial Isolation distances Downwind distances

## Slide 4
Table 3: Six common TIH (toxic by inhalation) Gases
Anhydrous Ammonia Chlorine Ethylene Oxide
Hydrogen Chloride Hydrogen Fluoride Sulfur Dioxide

## Slide 5
Chlorine – Rail tank car, Day
Isolate
1,000 meters (3,000 feet)
.62 mile
Protect Downwind
Moderate wind – 6 to 12 mph
4 miles

## Slide 6: What happens in a release? A footprint is formed
A release from one point source
Steady wind from one direction
Footprint that shows the furthest points the chemical reaches a given level (ppm)

## Slide 7: What health effects happen?
There are a number of health outcomes that responders use to utilize the ERG to plan a response inside and outside the downwind distance
Will people have mild symptoms? Can they escape? Have serious health effects? Are their lives threatened?

## Slide 8: Many models can show the three footprints (and health outcome areas) at same time
Impaired Escape
Death
Symptoms
No Symptoms

## Slide 9: They can also show the change of concentration at any given point for the first hour
Impaired Escape

## Slide 10: Scenario factors Chlorine tanker car in a Tucson, Arizona rail yard Full 90 ton car 1.5” hole at bottom of car Wind at 7 mph from east 70o at 8 AM, October 3 ERG p. 293: “determine the downward distance to which persons may become incapacitated and unable to take protective action or may incur serious health effects” Chlorine: 2 ppm for 60 minute exposure

## Slide 11: ALOHA Text Summary Site Data Chemical data Atmospheric data Source Strength Threat zone Threat at point

## Slide 12: Initial plume with threat zone marked on MARPLOT map at 2 miles
Death

## Slide 13: Concentration at 2 miles
Death 20 ppm

## Slide 14: Threat zone marked on MARPLOT map at 4 miles
Impaired Escape

## Slide 15: Concentration at 4 miles
Death
Ability to escape – 2 ppm

## Slide 16: Threat zone marked on MARPLOT map at 6 miles (limit of this program)
Symptoms
Impaired Escape
Symptoms

## Slide 17: Concentration at 6 miles
Ability to escape

## Slide 18
Impaired Escape, serious health effects and death population: 4.27 sq. miles; 11,945 people: 3,564 housing units
Impaired Escape/Death

## Slide 19
JENNIFER HOLLAND Associated Press
January 6, 2005
GRANITEVILLE, S.C. (AP) -- Townspeople and nightshift workers at a textile mill heard the scrape of metal and a house-shaking boom. Then, in rolled a greenish-yellow fog that smelled powerfully like bleach, searing their eyes and lungs and making them cough and gasp.
Chlorine Gas Still Lingers From South Carolina Train Wreck That Killed Eight