## Slide 1: Underground Natural Gas Storage
American Gas Association
Virtual Operations Conference
June 09, 2020
Byron Coy PE
Sr. Technical Advisor
USDOT / PHMSA

## Slide 2: Summary Timeline
1992/2001/2004 | Underground Storage Incidents & Accidents
July/Sep - 2015 | API Recommended Practices : 1170 & 1171
October - 2015 | Aliso Canyon Incident
June - 2016 | PIPES Act, Section 12
July - 2016 | Denver Public Workshop
December - 2016 | Interim Final Rule Published
May - 2017 | Revised IOGCC Regulatory Guidance
June - 2017 | Stay of Enforcement (non-mandatory provisions)
February - 2020 | Final Rule Published

## Slide 3
California
Inter UNGS: 0 Intra UNGS: 14
CA
OR
NV
WA
Oregon
Inter UNGS: 0 Intra UNGS: 1
ID
MT
Montana
Inter UNGS: 1 Intra UNGS: 3
WY
UT
CO
AZ
NM
TX
OK
Oklahoma
Inter UNGS: 5 Intra UNGS: 8
AR
Arkansas
Inter UNGS: 0 Intra UNGS: 2
Louisiana
Inter UNGS: 13 Intra UNGS: 5
ND
SD
LA
NE
IA
MO
KS
Kansas
Inter UNGS: 11 Intra UNGS: 6
MN
Minnesota
Inter UNGS: 0 Intra UNGS: 1
WI
Michigan
Inter UNGS: 19 Intra UNGS: 30
MI
Illinois
Inter UNGS: 6 Intra UNGS: 22
IL
IN
Indiana
Inter UNGS: 4 Intra UNGS: 16
OH
Ohio
Inter UNGS: 17 Intra UNGS: 3
PA
Pennsylvania
Inter UNGS: 42 Intra UNGS: 9
WV
West Virginia
Inter UNGS: 29 Intra UNGS: 3
VA
Virginia
Inter UNGS: 2 Intra UNGS: 0
NY
VT
ME
NH
MA
RI
CT
NJ
DE
MD DC
Maryland
Inter UNGS: 1 Intra UNGS: 0
New York
Inter UNGS: 26 Intra UNGS: 0
Kentucky
Inter UGSF: 6 Intra UGSF: 14
KY
TN
Tennessee
Inter UGSF: 0 Intra UGSF: 1
MS
Mississippi
Inter UGSF: 9 Intra UGSF: 2
AL
Alabama
Inter UGSF: 1 Intra UGSF: 1
Texas
Inter UNGS: 3 Intra UNGS: 29
New Mexico
Inter UNGS: 1 Intra UNGS: 1
Nebraska
Inter UNGS: 1 Intra UNGS: 0
Colorado
Inter UNGS: 6 Intra UNGS: 4
Wyoming
Inter UNGS: 5 Intra UNGS: 4
Utah
Inter UNGS: 3 Intra UNGS: 0
Washington
Inter UNGS: 1 Intra UNGS: 0
Iowa
Inter UNGS: 8 Intra UNGS: 0
Missouri
Inter UNGS: 0 Intra UNGS: 1
FL
SC
NC
GA
Underground Natural Gas Storage
PHMSA State Partners (CY2020)
Alaska
Inter UNGS:0 Intra UNGS: 4
AK
HI
PR
UNGS Intrastate 60105 Certification
UNGS Intrastate 60106 Agreement
States with no UNGS facilities
In Service Underground Natural Gas Storage (UNGS) counts as reported by operators
to PHMSA on Annual Reports as of July 2019.
Inspection agreement information updated April 2020.
Number of UNGS Facilities (green text)
Underground Natural Gas Storage Facilities in 31 States

## Slide 4: Facilities & Their Wells
 | Number of Facilities | % of Facilities |  | Number of Wells | % of Wells
Facilities to be Inspected by PHMSA | 302 | 80 |  | 14,590 | 85
Facilities to be Inspected by States | 79 | 20 |  | 2,592 | 15
Totals | 381 |  |  | 17,182 | 

## Slide 5
Federal Inspection of
Facilities and Wells
CY’s 2018 - 2020 | Facilities | Wells
2018 Inspections | 41 | 2100
2019 Inspections | 52 | 5500
2020 Inspections Planned | 70 | 2600
Totals | 163 | 10200

## Slide 6
Chart: Number of Inspections
| 43885 | 43892 | 43899 | 43899 | 43899 | 43906 | 43913 | 43913 | 43913 | 43920 | 43927 | 43927 | 43934 | 43955 | 43962 | 43983 | 43983 | 43990 | 43990 | 43997 | 43997 | 44004 | 44004 | 44004 | 44025 | 44025 | 44025 | 44032 | 44032 | 44032 | 44046 | 44046 | 44046 | 44053 | 44053 | 44053 | 44060 | 44060 | 44060 | 44067 | 44067 | 44067 | 44074 | 44074 | 44102 | 44102 | 44102 | 44109 | 44109 | 44109 | 44109 | 44109 | 44116 | 44116 | 44130 | 44151 | 44172
Confirmed | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57
Planned Goal | 70 | 0
Federal Inspections in CY-2020

## Slide 7
 | Total Inspection Count | Planned Questions | Completed Questions
2018 | 41 | 4,797 | 4,702
2019 | 53 | 5,610 | 5,604
Total | 94 | 10,407 | 10,306
Inspections & Question Sets

## Slide 8
 | Average SAT Percent per Inspection
2018 | 81.9 %
2019 | 82.9 %
Inspection Outcomes
Satisfactory Results

## Slide 9
Inspection Year | Average CONCERN Percent per Inspection
2018 | 15.0 %
2019 | 15.0 %
Inspection Outcomes
Concern Results

## Slide 10
Inspection Year | Average UNSAT Percent per Inspection
2018 | 1.19 %
2019 | 1.23 %
Inspection Outcomes
Unsatisfactory Results

## Slide 11
Start Year | # Planned Questions | Percent UNSAT’s
2019 | 52 | 13.5
2019 | 106 | 7.5
2019 | 106 | 7.5
2019 | 106 | 6.6
2019 | 106 | 6.6
2018 | 88 | 5.7
Individual Inspections
with Highest Shortfalls
Start Year | # Planned Questions | Percent CONCERN’s
2019 | 133 | 82.7
2018 | 121 | 81.0
2018 | 121 | 81.0
2018 | 111 | 40.5
2018 | 106 | 39.6

## Slide 12: Common Findings
Annular Gas
  Not monitoring for the presence of annular gas
  No established threshold pressure at which action must be taken
  Not evaluating each occurrence that exceeds operator-defined threshold
Emergency Response Plan
  Does not account for all required events
    Accidental Release
    Natural Disaster
    Equipment Failure
    Third Party Damage
  No program for periodic effectiveness testing

## Slide 13: Common Findings
Risk Model does not include third party wells or P&A wells
Preventive &Mitigative measures are not identified
Construction Notifications have not been made
No Blow-Out Contingency Plan

## Slide 14: Highest Percentage of Concern’s Top 5 Content Areas
Annular Gas Monitoring
  Threshold Limits & Exceedances Evaluation
Threats & Hazards
  Interactions & Exclusions, Threat Evaluation
Third Party Wells
  Documenting data requests, evaluation of 3rd Party data
Well Integrity Evaluations
  Documenting mechanical integrity of each well
Risk Assessments
  Periodic review & improvement cycle, effectiveness, applying results

## Slide 15: Highest Percentage of Unsat’s Top 5 Content Areas
Annular Gas Monitoring
  Threshold Limits, & Exceedance Evaluation
Blowout Contingency Plans
  Plan in place, review & update process
Emergency Plan, Periodic review for effectiveness
Well Maintenance & Inspections
  Visual inspections, master valve testing, valve maintenance, signage
Risk Assessments
  Review of results, accurate representation of risk

## Slide 16: Compliance Actions in 2018/2019 Proposed Notice of Amendments
Items citing 192.12(e)
  Establish and follow written procedures for operations, maintenance, and emergency preparedness requirements

## Slide 17: Compliance Actions in 2018/2019 Proposed Warning Letters
Items citing 192.12(d)
  Operations, maintenance, integrity demonstration and verification, monitoring, threat and hazard identification, assessment, remediation, site security, emergency response and preparedness, and recordkeeping requirements
Items citing 192.12(e)
  Establish and follow written procedures for operations, maintenance, and emergencies… implementing the requirements

## Slide 18
Enforcement Actions
01-01-18 thru 02-03-2020
Enforcement Initiated | Cases | Proposed NOA Items | Proposed Warning Items
2018 | 7 | 19 | 4
2019 | 14 | 28 | 9
2020 YTD | 7 | 9 | 7
Totals | 28 | 56 | 20

## Slide 19: Construction Notifications Regulation 191.22(c)(1)
Construction of a new UNGSF
Maintenance involving plugging or abandonment, or that requires a workover rig and costs $200,000 or more for an individual well, including its wellhead
60 days before the event occurs (or commences)
If 60-day notice is not feasible because of an emergency, notify PHMSA as soon as practicable

## Slide 20
Notifications | 
Intrastate | 188
Interstate | 267
Total | 455
Construction Notifications
Oct-2016 thru Apr-2020
Activities | 
New Well | 36
Workover | 330
P&A | 140
Integrity | 77
Total | 583
Wells Impacted | 2438
A notification can include multiple activities

## Slide 21
Construction Notification Timing
After Work Started | 37
When Work Started | 7
1-29 Days in Advance | 61
30-59 Days in Advance | 70
60-89 Days in Advance | 216
90+ Days in Advance | 64
191.22(c)(1)
If 60-day notice is not feasible because of an emergency, notify PHMSA as soon as practicable
Notation in records

## Slide 22
Construction Notification Duration
0 or Blank | 58
1 - 7 Days | 26
8 – 14 Days | 26
15 – 29 Days | 40
30 – 59 Days | 85
60 – 179 Days | 103
180+ Days | 117

## Slide 23: Final Rule
Restored Non-Mandatory Provisions for Recommended Practices
Narrowed Scope for Construction Notifications
Roles and Responsibilities must be defined

## Slide 24: Final Rule
March 13, 2024 : Complete the baseline risk assessments of all reservoirs/caverns, and 40% of wells/wellheads
March 13, 2027 : Complete baseline risk assessments on all its wells/wellheads
Seven year assessment interval
Salt Caverns must follow RP-1171 Risk Management, Section 8, as applicable

## Slide 25: 191.3, Incident
An event that results in an emergency shutdown of an LNG facility or a UNGSF
Activation of an emergency shutdown system for reasons other than an actual emergency within the facility does not constitute an incident

## Slide 26: 191.23(b)(5) Safety-Related Condition
(b) A report is not required for any safety-related condition that -
(5) Exists on an UNGSF, where a well or wellhead is isolated, allowing the reservoir or cavern and all other components of the facility to continue to operate normally and without pressure restriction.

## Slide 27: After the Final Rule
Revised Inspection Question Set
Revised FAQ’s
Reformed TQ Inspector Training Classes
Workshop
Initiation of Annual UGS Conference

## Slide 28: Changes prompted by Final Rule
 | FAQs |  |  | IA Questions |  | 
 | Current Count | Edit or Delete | Create New | Current Count | Edit or Delete | Create New
191 | 3 | 2 | 1 | 14 | 11 | 0
192 | 18 | 18 | 4 | 462 | 400 | 10
Preliminary Analysis

## Slide 29: PHMSA : Web Links
http://www.phmsa.dot.gov
Resources/Technical Resources/Underground NG
  Key Documents
  Locations
  Major Incidents
  Pictures & Diagrams
  State Participation
  Technical Reports
https://www.phmsa.dot.gov/forms/pipeline-forms
https://www.transportation.gov/regulations

## Slide 30: Contact Information
Byron Coy PE
Sr. Technical Advisor
USDOT / PHMSA
byron.coy@dot.gov
609-771-7810